smartTFT

Control TFT and TFT Touch Displays remotely

# Brief description

There is a lot of small and cheap color TFT displays around and with this project I want to give some of them the possibility to remotely control its content. Control is done by most common function calls of the Arduino GFX Library that are transferred to a µController that executes them.
µControllers that may be used are several typed of Arduino (e.g. Pro Mini) and the ESP8266 Series as well as the ESP32xx Series SoCs.
 The displays that are suitable to use are the several 0.96“, 1.2“, 1.8“, 2.2“ … TFT displays and TFT displays with touch interface.
For more information about µControllers and displays see appendix A.
# Proof of concept and 1st prototype

First prototype and proof of concept is done with a ST7735 based 1.8" TFT with an additional SD-card slot.
As a µController an Arduino Pro Mini is used.
Communication is done using the UART of the Arduino.
A self-made case will hold the components.
A buzzer is used to realize an alarm-function, a LDR makes ist possible to change brightness of the display depending on ambient light.

## Prototype Electronic Components
### Parts List

- 1 x Arduino Pro Mini
- 1 x 1.8" TFT with SD-slot
- 2 x Levelshifter with 4 channels
- 1 x Stepup/Stepdown Regulator 5 <-> 3V3
- 1 x LDR
- 1 x Buzzer
- 1 x Resistor 10 kOhm
- 2 x Resistor 4.7 kOhm
- 1 x Resistor 100 Ohm
- 2 x Ceramic Capacitor 100 nF
- 1 x Proto-PCB 16 rows/32 columns (around 42 x 83 mm)
- 1 x Proto-PCB 16 rows/6 columns (around 42 x 15 mm)
- 1 x Stereo Jack female 3.5 mm
- 1 x DC Jack female 3.5 mm x 1.1 mm
- 1 x 4x1 Pin Header
- a bunch of colored wires 0.14 mm

Wiring via Levelshifter
--
| Arduino | Levelshifter| Levelshifter|1.8" TFT |
|--|--|--|--|
| Pin #10 |HV*| LV** | TFT_CS |
| Pin #9 |HV| LV|TFT_RST |
| Pin #8 |HV| LV|TFT_DC |
| Pin #13 |HV| LV|TFT_SCL |
| Pin #11 |HV| LV|TFT_SDA |
| Pin #7 |HV| LV|SD_CS |
| Pin #12 |HV| LV|SD_MISO |
| Pin #11 |HV| LV|SD_MOSI|
| Pin #13 |HV| LV|SD_SCL |

*HV means High Voltage Side
**LV means Low Voltage Side

---

Because Vcc of the TFT is 5V **be aware** that **Jumper J1** on the back side of TFT is **open!** Otherwise the display is damaged.

Direct Wiring
--
|Arduino|Target 1 | Target 2| is for |
|--|--|--|--|
|Pin #5 | 100 Ohm | buzzer | limit current |
|Pin #6 | TFT LED+ | -- |dim backlight |
|Pin A0 | LDR |-- | light sense |
|Pin A0 | 10 kOhm |GND | pulldown|

Realized GFX-functions
--
 - drawLine()
 - drawFastHLine()
 - drawFastVLine()
 - drawRect()
 - fillRect()
 - drawCircle()
 - fillCircle()
 - drawTriangle()
 - fillTriangle()
 - drawRoundRect()
 - fillRoundRect()
 - setRotation()
 - setTextWrap()
 - fillScreen()
 - setTextColor()
 - fillScreen()
 - invertDisplay()
 - drawCircleHelper()
 - fillCircleHelper()
 - drawBitmap()
 - drawChar()
 - setCursor()
 - setTextSize()
 - height()
 - width()
 - write()
 - drawPixel()
 - print()
 - println()

and. last but not least,
- setbrightness()

for dimming backlight of the TFT Display.