Brief description
--
There is a lot of small and cheap color TFT displays around and with this project I want to give some of them the possibility to remotely control its content. Control is done by most common function calls of the Arduino GFX Library that are transferred to a µController that executes them.

First Prototype
--
First prototype is a 1.8" TFT with a ST7735 controller and additional SD-card slot.
As a µController an Arduino Pro Mini is used.
Communication is done using the UART of the Arduino.
A self-made case will hold the components.
A buzzer is used to realize an alarm-function, a LDR makes ist possible to change brightness of the display depending on ambient light.

***Be aware ... this is a work-in-progress project. Some parts may not or not proper work. Use at your own risc!***

Parts List 1st Prototype
--
 - 1 x Arduino Pro Mini 1 x 1.8" TFT with SD-slot
 - 2 x Levelshifter with 4 channels
 - 1 x Stepup/Stepdown Regulator 5 <-> 3V3
 - 1 x LDR
 - 1 x Buzzer
 - 1 x Resistor 10 kOhm
 - 2 x Resistor 4.7 kOhm
 - 1 x Resistor 100 Ohm
 - 2 x Ceramic Capacitor 100 nF
 - 1 x Proto-PCB 16 rows/32 columns (around 42 x 83 mm)
 - 1 x Proto-PCB 16 rows/6 columns (around 42 x 15 mm)
 - 1 x Stereo Jack female 3.5 mm
 - 1 x DC Jack female 3.5 mm x 1.1 mm
 - 1 x 4x1 Pin Header
 - a bunch of colored wires 0.14 mm

Wiring via Levelshifter
--
| Arduino | Levelshifter| Levelshifter|1.8" TFT |
|--|--|--|--|
| Pin #10 |HV*| LV** | TFT_CS |
| Pin #9 |HV| LV|TFT_RST |
| Pin #8 |HV| LV|TFT_DC |
| Pin #13 |HV| LV|TFT_SCL |
| Pin #11 |HV| LV|TFT_SDA |
| Pin #7 |HV| LV|SD_CS |
| Pin #12 |HV| LV|SD_MISO |
| Pin #11 |HV| LV|SD_MOSI|
| Pin #13 |HV| LV|SD_SCL |

*HV means High Voltage Side
**LV means Low Voltage Side

---

Because Vcc of the TFT is 5V **be aware** that **Jumper J1** on the back side of TFT is **open!** Otherwise the display is damaged.

Direct Wiring
--
|Arduino|Target 1 | Target 2| is for |
|--|--|--|--|
|Pin #5 | 100 Ohm | buzzer | limit current |
|Pin #6 | TFT LED+ | -- |dim backlight |
|Pin A0 | LDR |-- | light sense |
|Pin A0 | 10 kOhm |GND | pulldown|

Realized GFX-functions
--
 - drawLine()
 - drawFastHLine()
 - drawFastVLine()
 - drawRect()
 - fillRect()
 - drawCircle()
 - fillCircle()
 - drawTriangle()
 - fillTriangle()
 - drawRoundRect()
 - fillRoundRect()
 - setRotation()
 - setTextWrap()
 - fillScreen()
 - setTextColor()
 - fillScreen()
 - invertDisplay()
 - drawCircleHelper()
 - fillCircleHelper()
 - drawBitmap()
 - drawChar()
 - setCursor()
 - setTextSize()
 - height()
 - width()
 - write()
 - drawPixel()
 - print()
 - println()

and. last but not least,
- setbrightness()

for dimming backlight of the TFT Display.